## Slide 1: FLSM Last Update 2012.09.29 1.4.0

## Slide 2: Objectives of This Section
Learn how to do Fixed Length Subnet Masking

## Slide 3: What is Subnetting
What is subnetting
Subnetting is where bits are taken from the host portion of the IP address and used to create subnetworks
In other words new networks that exist below or subordinate to larger networks
The original largest networks were those 256 networks

## Slide 4: Let’s Switch Gears
Now before we can learn to subnet we need to sidestep from the discussion of the network addressing to discuss numbering systems conversions as we will need to be able to do this so we can learn how subnetting is done

## Slide 5: Numbering Systems of Interest
We need to be able to convert in our heads back and forth between decimal and binary numbering systems
  Base 10 – Decimal
  Base 2 – Binary

## Slide 6: Base 10 Numbers
Humans use decimal numbers
Computers do not use these

## Slide 7: Base 2 Numbers
Computers use the binary number system as they are composed of transistors for the most part
Recall that these are simple on off devices
This is easily represented by 0 or 1 in a numbering system

## Slide 8: Conversion of Decimal to Binary
A common task is to convert a decimal number to a binary number
To do this one must first learn the bit positions

## Slide 9: Binary Bit Positions
Reading from left to right
Bit Position | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1

## Slide 10: Binary Bit Positions
Each of these bit positions has a value
Bit Position | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
Value | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1

## Slide 11: Conversion of Decimal to Binary
To convert a decimal to a binary number use the bit position values to find the binary number that equals the decimal number
For example

## Slide 12: Conversion of Decimal to Binary
To convert 168 into binary
  Moving from left to right, if the value for the bit position is less than or equal to the decimal number assign a 1 to that bit position in the binary number
  If it does not, then assign a 0
  Then subtract that bit position value from the remainder
  Go to the next bit position and do the same thing

## Slide 13: Conversion of Decimal to Binary
8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
Add the numbers where 1s are together
The result should be the decimal number

## Slide 14: Conversion of Binary to Decimal
To convert from binary to decimal do the reverse
Add the decimal values of the binary position values where a 1 is used
For example
  10011011
8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 0 | 0 | 1 | 1 | 0 | 1 | 1

## Slide 15: Conversion of Binary to Decimal
The result is
  155

## Slide 16: Conversion of Binary to Decimal

## Slide 17: ANDing Binary Numbers
Binary numbers can be added together to yield a new number
This is called ANDing
We will use this procedure below
To AND two binary numbers
  A 1 and a 1 is a 1
  A 0 and anything is a 0

## Slide 18: Reasons for Subnetting
Back to subnetting
Over the years the method developed for IP addressing did not generate enough network addresses
To help this subnetting was developed
To be a proper networking nerd you must understand subnetting

## Slide 19: Reasons for Subnetting
The first step in this understanding is said to be to learn to subnet using only your brain
I know this is a scary thought
But you must learn to do this

## Slide 20: How to Think About Subnetting
Subnetting is easy to understand
Let’s use an analogy
Suppose you buy a piece of land at the end of a road with the intention of building houses on it
For example

## Slide 21: How to Think About Subnetting
End of the Road
We Are
Going to Build Houses Here

## Slide 22: Our Road Layout
To build houses on this land we must build roads on it, then build houses on those roads
For example

## Slide 23: Our Road Layout
Our New Roads
The Houses On Each Road

## Slide 24: How to Think About Subnetting
Just like a subdivision you are going to have to figure out how many roads you need for the subdivision plus how many houses to build on each road
Once the roads are in place you need to know that the house numbers will be on each road
This is all there is to subnetting
It is exactly the same thing

## Slide 25: General Approach
As we will learn later on there is no such thing as address classes anymore
However when doing this in your head subnetting is much easier if you do it based on address classes
Which is way you had to learn about the old address classes

## Slide 26: The Basics
Recall that the purpose of a subnet mask is to allow a device to know what part of the address represents the network and what part the host
To create a subnet, bits are taken from the host portion of the address
  This will mean fewer bits for the host
  And the same number of bits for the network
Remember we are creating not a network, but a subnetwork

## Slide 27: The Basics
First, memorize the Powers of 2
  21 = 2
  22 = 4
  23 = 8
  24 = 16
  25 = 32
  26 = 64
  27 = 128
  28 = 256

## Slide 28: The Basics
Second, recall the Bit Position Values
  8 = 128
  7 = 64
  6 = 32
  5 = 16
  4 = 8
  3 = 4
  2 = 2
  1 = 1

## Slide 29: The Basics
Third, try to memorize the Bit Patterns
  10000000 = 128
  11000000 = 192
  11100000 = 224
  11110000 = 240
  11111000 = 248
  11111100 = 252
  11111110 = 254
  11111111 = 255

## Slide 30: Notice the Pattern

## Slide 31: Notice the Pattern
As a bit is stolen to create a subnet the number of subnets doubles and the number of hosts on any subnet is cut in half

## Slide 32: Subnetting by Hand Methods
There are several ways to do subnetting by hand or using only your brain
We will cover two of these
They are
  The Five Question Method
  / Notation Method

## Slide 33: The Five Question Method
Answer the following questions
  How many networks can we create
  How many devices can be on each network
  What are the network names
  What are the device names
  What is the broadcast address of each subnet

## Slide 34: Subnetting a Class C Address
In the case of a Class C address bring to mind the standard mask for a Class C address of 255.255.255.0
Notice that this leaves only the last octet for use by both the subnetwork and the host
So we only have 8 bits to work with

## Slide 35: Subnetting a Class C Address
How many networks can we create
Formula
  2N = Number of Subnets
    Where N is the number of bits stolen for the subnetwork

## Slide 36: Subnetting a Class C Address
For example
  00000000 20 = Not used creates no subnets
  10000000 21 = 2 subnetworks using the 128 mask
  11000000 22 = 4 subnetworks using the 192 mask
  11100000 23 = 8 subnetworks using the 224 mask
  11110000 24 = 16 subnetworks using the 240 mask
  11111000 25 = 32 subnetworks using the 248 mask
  11111100 26 = 64 subnetworks using the 252 mask
  11111110 27 = Not used as no hosts are left
  11111111 28 = Not used as no hosts are left

## Slide 37: Subnetting a Class C Address
How many devices can be on the network
Formula
  2H – 2 = Number of Hosts per Subnet
    Where H is the number of bits left for the hosts after the subnet is created

## Slide 38: Subnetting a Class C Address
For example
  00000000 - 28 - 2 = Not used creates no subnets
  10000000 - 27 - 2 = 126 using the 128 mask
  11000000 - 26 - 2 = 62 using the 192 mask
  11100000 - 25 - 2 = 30 using the 224 mask
  11110000 - 24 - 2 = 14 using the 240 mask
  11111000 - 23 - 2 = 6 using the 248 mask
  11111100 - 22 - 2 = 2 using the 252 mask
  11111110 - 21 - 2 = Not used as no hosts left
  11111111 - 20 - 2 = Not used as no hosts left

## Slide 39: Subnetting a Class C Address
What are the network names
Formula
  0 is the first network number
  Then 256 – the subnet mask number in decimal is the base number
  The base number is the second subnetwork number
  The base number plus the last subnetwork number is the next subnetwork number
  Until the subnet number in decimal is reached which is the last subnetwork number

## Slide 40: Subnetting a Class C Address
For example
  Three bits were used so 224 is the subnet mask number
  256 – 224 = 32
  32 then is the base number
  Therefore

## Slide 41: Subnetting a Class C Address
  0
  32
  32+32=64
  64+32=96
  96+32=128
  128+32=160
  160+32=192
  192+32=224
The eight subnetwork numbers then are
  0-32-64-96-128-160-192-224

## Slide 42: Subnetting a Class C Address
What are the device names on each network
Formula
  The Numbers Between Each Subnet Number, except for the last number
For example

## Slide 43: Subnetting a Class C Address
Subnetwork Numbers |  |  |  |  |  |  | 
0 | 32 | 64 | 96 | 128 | 160 | 192 | 224
Host Address Range |  |  |  |  |  |  | 
1 | 33 | 65 | 97 | 129 | 161 | 193 | 225
30 | 62 | 94 | 126 | 158 | 190 | 222 | 254

## Slide 44: Subnetting a Class C Address
What is the broadcast address for each network
Formula
  The number with all the bits turned on
  or
  The number just before the next subnet number
For example

## Slide 45: Subnetting a Class C Address
Subnetwork Numbers |  |  |  |  |  |  | 
0 | 32 | 64 | 96 | 128 | 160 | 192 | 224
Broadcast Address |  |  |  |  |  |  | 
31 | 63 | 95 | 127 | 159 | 191 | 223 | 255

## Slide 46: The / Notation Method
Here is a another method which may prove easier for you
  Go from / notation to
  The subnet mask to
  The network addresses to
  The number of hosts
For example

## Slide 47: The / Notation Method
With a /26
A subnet mask of 255.255.255.192
Network address block size of 256 minus the subnet number
  For example, 256-192=64
    0
    64
    128
    192

## Slide 48: The / Notation Method
Number of hosts network size-2
  64-2
    62

## Slide 49: Subnetting a Class B Address
On to the Class B address
The default subnet mask for a Class B address is
  255.255.0.0
Notice that we now have two octets or 16 bits to work with
So the valid subnet masks are

## Slide 50: Subnetting a Class B Address
For the third octet, all of which may be stolen
  1 bit stolen - 255.255.128.0
  2 bits stolen - 255.255.192.0
  3 bits stolen - 255.255.224.0
  4 bits stolen - 255.255.240.0
  5 bits stolen - 255.255.248.0
  6 bits stolen - 255.255.252.0
  7 bits stolen - 255.255.254.0
  8 bits stolen - 255.255.255.0

## Slide 51: Subnetting a Class B Address
If the third octet is used since this is a Class B address the third octet may be used as well
  9 bits stolen - 255.255.255.128
  10 bits stolen - 255.255.255.192
  11 bits stolen - 255.255.255.224
  12 bits stolen - 255.255.255.240
  13 bits stolen - 255.255.255.248
  14 bits stolen - 255.255.255.252
  Stop here as the RFCs say at least two bits must be left

## Slide 52: Subnetting a Class A Address
On to the Class A address
The default subnet mask for a Class A address is
  255.0.0.0
Notice that we now have three octets or 24 bits to work with
So the valid subnet masks are

## Slide 53: Subnetting a Class A Address
For the second octet, all of which may be stolen
  1 bit stolen - 255.128.0.0
  2 bits stolen - 255.192.0.0
  3 bits stolen - 255.224.0.0
  4 bits stolen - 255.240.0.0
  5 bits stolen - 255.248.0.0
  6 bits stolen - 255.252.0.0
  7 bits stolen - 255.254.0.0
  8 bits stolen - 255.255.0.0

## Slide 54: Subnetting a Class A Address
The third octet maybe used since this is a Class A address
  9 bits stolen - 255.255.128.0
  10 bits stolen - 255.255.192.0
  11 bits stolen - 255.255.224.0
  12 bits stolen - 255.255.240.0
  13 bits stolen - 255.255.248.0
  14 bits stolen - 255.255.252.0
  15 bits stolen – 255.255.254.0
  16 bits stolen – 255.255.255.0

## Slide 55: Subnetting a Class A Address
If the fourth octet is used
  17 bits stolen - 255.255.255.128
  18 bits stolen - 255.255.255.192
  19 bits stolen - 255.255.255.224
  20 bits stolen - 255.255.255.240
  21 bits stolen - 255.255.255.248
  22 bits stolen - 255.255.255.252
  Stop here as the RFCs say at least two bits must be left

## Slide 56: A Final Note on This Procedure
What is the point in all of this
Once you get past the old Class C examples above the actual listing of the bit patterns, the subnet numbers, the host addresses, and so on gets so lengthy and so prone to typical human error and typos that what’s the point
No one would actually do this
So we will stop here

## Slide 57: Decimal Method Subnetting
David Schamus in a presentation for the 2011 Cisco Academy Conference presented another method for subnetting by hand
This method uses only simple arithmetic
I have changed the names of the parts in some cases
Let’s look at it

## Slide 58: Network Address
First what is the network address for a combination of IP address and subnet mask
The IP address in this example is
  10.1.1.84
The subnet mask is
  255.255.255.224

## Slide 59: Network Address
As this subnet is not on a fixed length boundary such as 255.255.255.0 the network address is not obvious by just looking at the two
We will calculate it

## Slide 60: Network Address
The procedure is
  256 - The Subnet Mask Number = Result 1
  The IP Address Shown / Result 1 = Result 2
    For Result 2 ignore the decimal places
  Result 2 * Result 1 = The Network Number
  Put this number in the octet with the non 255

## Slide 61: Network Address
For example
  256 – 224 = 32
  84 / 32 = 2
  2 * 32 = 64
  We were given 10.1.1.84 255.255.255.224
  The network address is then 10.1.1.64

## Slide 62: Network Address
Let’s look at another example
  172.31.33.84
  255.255.240.0
  256 - 240 = 16
  33 / 16 = 2
  16 * 2 = 32
  172.31.32.0
Here are four more examples using his naming

## Slide 63: Network Address

## Slide 64: Broadcast Address
This just adds one more step to the Network Address procedure
This step is
  Network Address + Result 1 – 1
  64 + 32 – 1 = 95
  In the first example above this would result in
    10.1.1.95
  as the broadcast address

## Slide 65: Broadcast Address
For the 172.31.33.84 255.255.240.0 example
32 + 16 – 1 = 47
172.31.47.255 is the broadcast address
Another example using his naming scheme

## Slide 66: Broadcast Address

## Slide 67: Host Addresses
Now what are the host addresses on the network
This is just all the addresses between the network address and the broadcast address
For example

## Slide 68: Host Addresses
We were given 10.1.1.84 255.255.255.224
  The network address is then 10.1.1.64
  Because
    256 – 224 = 32
    84 / 32 = 2
    2 * 32 = 64

## Slide 69: Host Addresses
  And the broadcast address is
  Because
    Network Address + Result 1 – 1
    64 + 32 – 1 = 95
  This would result in
    10.1.1.95
  as the broadcast address
  So the brackets are
    10.1.1.64 and 10.1.1.95

## Slide 70: Host Addresses
The host addresses are
  65 to 94
Some example using his naming scheme

## Slide 71: Host Addresses

## Slide 72: A Subnet Calculator
Well that was all fascinating
Yes you are correct
No one does it this way in the real world
They use a subnet calculator
Let’s look at one
Go to www.boson.com