## Slide 1: Route Redistribution
Last Update 2012.01.25
1.0.0

## Slide 2: Objectives
Learn about redistributing routes between different routing protocols

## Slide 3: Route Redistribution
By design a routing protocol will only share routes it knows about with routers running the same routing protocol
In other words, OSPF only talks to OSPF, EIGRP to EIGRP, and RIP to RIP

## Slide 4: Route Redistribution
In the case where one router is populating its routing table using say OSPF while its neighbor is using EIGRP for that purpose in order for a route learned by OSPF to be used by a router using EIGRP that route must be injected or distributed into the other routing protocol

## Slide 5: Route Redistribution
Route redistribution then allows two different routing protocols to share and advertise routes to each other
For example, let’s say we have three routers in a row
Such as

## Slide 6: Route Redistribution

## Slide 7: OSPF Only
enable
config t
int s0/0/0
ip address 192.168.1.1 255.255.255.0
no shutdown
clock rate 64000
exit

## Slide 8: OSPF Only
router ospf 1
network 192.168.1.0 0.0.0.255 area 0
end

## Slide 9: OSPF and EIGRP
enable
config t
in s0/0/0
ip address 192.168.1.2 255.255.255.0
no shutdown

## Slide 10: OSPF and EIGRP
int s0/0/1
ip address 192.168.2.1 255.255.255.0
no shutdown
clock rate 64000
exit

## Slide 11: OSPF and EIGRP
router ospf 1
network 192.168.1.0 0.0.0.255 area 0
router eigrp 1
network 192.168.2.0
end

## Slide 12: EIGRP Only
enable
config t
int s0/0/1
ip address 192.168.2.2 255.255.255.0
no shutdown
exit

## Slide 13: EIGRP Only
router eigrp 1
network 192.168.2.0
end

## Slide 14: Routing Tables
The result is for the
  OSPF Only router
    C 192.168.1.0/24 is directly connected, Serial0/0/0
  EIGRP Only Router
    C 192.168.2.0/24 is directly connected, Serial0/0/1
  OSPF and EIGRP Router
    C 192.168.1.0/24 is directly connected, Serial0/0/0
    C 192.168.2.0/24 is directly connected, Serial0/0/1

## Slide 15: Route Redistribution is Added
Now the route redistribution command is added to the OSPF and EIGRP router
  router ospf 1
  redistribute eigrp 1
The route says
  % Only classful networks will be redistributed

## Slide 16: Route Redistribution is Added
And for the other way
  router eigrp 1
  redistribute ospf 1 metric 10000 10 255 1 1500

## Slide 17: Route Redistribution is Added
When redistributing ospf a few metrics must be specified at the end of the command
These are
  Bandwidth in kbps
  Delay in microseconds
  Reliability from 0 to 255 where 255 is best
  Loading from 0 to 255 where 255 fully loaded
  MTU such as 1500 bytes

## Slide 18: Route Redistribution is Added
Now we see in the OSPF Only router
  C 192.168.1.0/24 is directly connected, Serial0/0/0
  O E2 192.168.2.0/24 [110/20] via 192.168.1.2, 00:02:30, Serial0/0/0

## Slide 19: Route Redistribution is Added
And in the EIGRP Only router
  D EX 192.168.1.0/24 [170/3072256] via 192.168.2.1, 00:00:29, Serial0/0/1
  C 192.168.2.0/24 is directly connected, Serial0/0/1