## Slide 1: RFID
Last Update 2008.12.06
1.0.0

## Slide 2: What is RFID
RFID devices are Radio Frequency Identification Devices
Here is a good explanation of what they do from RFID Network Implications by Ron Passmore
  Simply described, RFID is the use of electronic tags that replace printed bar codes on shipped items for tracking of their location
  RFID can be thought of as “radio barcodes”

## Slide 3: RFID
  However, RFID tags are different from UPC (universal product code) labels in that the tags don’t have to be visible, they can maintain state information, and the tags can be modified by the reader via 2-way communications
  This means that RFID tags must have active electronics, but since they have no batteries or other power source built-in, all of the power to activate an RFID tag’s circuitry must come from the RFID reader, via electromagnetic radiation

## Slide 4: RFID
  The tag readers must send energy to the tag to “wake it up,” after which the tag can transmit back its information contents
  The tags themselves consist of very tiny microchips smaller than a pin head
  The chips can be encased in a paper sticker upon which an antenna can be printed using special ink

## Slide 5: RFID
  To avoid safety issues or interference with other devices, the power radiated by RFID readers cannot be too strong
  This means that the readers must be located very close to (within a meter or two of) the tagged item being read, in order to turn on the tag
  Therefore readers must be widely distributed to those locations where they can be in close proximity to the items being tracked

## Slide 6: RFID in Action
Let’s see what RFID could do for us

## Slide 7: Review
Where could RFID be used